## Slide 1: ESP Well Failure Prediction
30-Day Early Warning System Using Random Forest
Regnold Chinowaita & Diego De la Cruz Torres

## Slide 2: Introduction
Problem
  ESP (Electrical Submersible Pump) failures cause costly unplanned shutdowns in oil wells
  Reactive maintenance = expensive downtime + lost production
  Harsh downhole environments (sand, heat) reduce ESP life to ~2 years
Goal
  Predict ESP failure up to 30 days in advance using sensor and production data
  Output: failure probability per well + CRITICAL / HIGH / MEDIUM / LOW risk tier
Why Machine Learning?
  Sensor degradation patterns are non-linear and subtle — rule-based systems miss them
  Random Forest handles mixed sensor types, missing values, and class imbalance well
Industry Value
  Enables scheduled maintenance, reducing downtime and workover costs by millions per well
  Provide operators enough time to schedule rigs and order replacement pumps

## Slide 3: Data Description
Source
  E-Challenge competition dataset — historical ESP sensor and production data from deepwater wells Ecuador Section
Scale
  94 labeled training wells + 15 held-out test wells
  High-frequency sensor readings (intra-day) + daily production reports
Sensor Inputs (X)
  Vibration, Intake Pressure, Motor Temperature, Current, Frequency, BOPD, BFPD
Target (Y)
  Binary: will this well fail within the next 30 days? (1 = Yes, 0 = No)
Class Imbalance Challenge
  Failures are rare (~0.2% of rows)
  SMOTE (Synthetic Minority Over-sampling Technique) is a data balancing method used when failures are rare.

## Slide 4: Data Pre-Processing
Step 1 — Temporal Alignment (structurer)
  Sensor data (intra-day) and production data (daily) have different frequencies
  Custom structurer function: resamples production to daily cadence, forward-fills gaps, matches each production day to nearest sensor snapshot (±1 day)
Step 2 — Downsampling (frequency_modifier)
  Multiple sensor readings per day averaged to one row per well per day
Step 3 — Feature Engineering
  Outlier clipping at 1st–99th percentile per well
  Imputed missing values with median per well
  Ratio features added: BOPD/FREQ*60, BFPD/FREQ*60, PRESS_INT/PRESS_DESC
Step 4 — Label Engineering
  7-day pre-failure window flagged as “failure approaching”; 30-day lookahead target created

## Slide 5: Sensor Trends Before Failure
Vibration: Rising mechanical wear and bearing friction.
Current: Sharp increases as the motor struggles with torque load.
Efficiency (BOPD/FREQ*60): Fluid production drops even at high speeds.
7-Day Window: A distinct degradation "signature" appears right before a crash

## Slide 6: Methodology
Algorithm: Random Forest Classifier
  100 trees; max depth tuned via k-fold cross-validation; class_weight=“balanced” applied
Class Imbalance: SMOTE Oversampling
  Failures are rare (~0.2%). SMOTE generates synthetic minority samples on the training set only — test set kept untouched
Train/Test Split
  94 wells for training, 15 wells completely held out for final evaluation (no data leakage)
Deployment Output
  P₀₃₀ = 1 − (1 − Pavg)³⁰ and 5-day rolling alert days → CRITICAL / HIGH / MEDIUM / LOW risk tier per well

## Slide 7: Results — Classification Performance
Precision (failures): 64% • Recall (failures): 91% • F1: 0.75 • AUC: 0.992 — Model correctly catches 91% of real failures with only 78 false alarms out of 4,014 normal days

## Slide 8: Results — What Drives Failure?
Key Takeaways
• VIBRATION is the #1 predictor — rising vibration is the earliest failure signal
• PRESS_INT and CURRENT together account for 31% of model decisions
• BOPD/FREQ ratio captures production efficiency loss before visible symptoms
• Bottom 3 features add minimal signal — could be dropped to simplify model
Top 3 features alone explain 52% of model behaviour

## Slide 9: Results — 30-Day Risk Dashboard (Test Wells)
Wells 38, 43, 39, 40, 48, 42, 46, 37, 50 exceed the 50% failure threshold. Only wells 38 and 37 show sustained alert days — most wells hit high probability briefly rather than persistently.

## Slide 10: Conclusions
Random Forest achieves AUC = 0.992, detecting 91% of real ESP failures.
The model provides reliable 30-day advance warning across 15 unseen test wells.
Vibration, intake pressure, and current are the three strongest failure indicators.
SMOTE effectively addressed class imbalance without introducing data leakage.
The risk dashboard translates model output into actionable CRITICAL/HIGH/MEDIUM/LOW tiers.
5 of 15 test wells were correctly flagged CRITICAL, enabling prioritised maintenance planning.
Future work: incorporate real-time streaming data and test XGBoost / LSTM for comparison.